## Slide 1
Field and Service Robotics: Technical Report
Fabio Ruggiero 2024/2025
Students:
Gianmarco Corrado P38000287
Andrea Colapinto P38000309

## Slide 2
Project Overview

## Slide 3
Mission Objectives & Implementation
The UAV's mission is to navigate a cluttered 3D indoor environment, pass through a narrow opening, and hover precisely at a target location.
Full Nonlinear Dynamic Model for a tilting
quadrotor
UAV with tilt-rotor actuation dynamics.
Polynomial-Based Trajectory Planning and 3D environment
Structured indoor environment and smooth path generation.
Aerodynamic Effects and Disturbances
Integration
Ground and ceiling interactions and robustness analysis.
Simulink and MATLAB-Based NMPC
Controller
Optimal control input computation with Voliro approach.

## Slide 4
Dynamic Model
Nonlinear model consisting of 6 inputs, 13 states and 13 outputs.
Representation in ENU frame
Orientation is represented using a unit quaternion to avoid singularities and maintain a column vector format.

## Slide 5
Aerodynamic Effects
Aerodynamic effects like ground and ceiling interactions significantly influence thrust efficiency near surfaces.
Ground Effect
Ceiling Effect

## Slide 6
Reference Trajectory Planning
Indoor environment navigation by following a path.
Waypoints based trajectory interpolated using splines.
Moving average filter applied to smooth the trajectory.
Waypoints matrix
Moving average filter

## Slide 7
Nonlinear Model Predictive Control (NMPC)
NMPC predicts future behavior over a finite horizon N
Optimization problem is to minimize a cost function while satisfying constraints.

## Slide 8
Simulink Implementation
Block scheme of the control logic:

## Slide 9
Simulation Results: Default Case
The NMPC controller demonstrates accurate trajectory tracking.

## Slide 10
Simulation Results: Disturbed Case
The NMPC controller maintains precise trajectory tracking even in the presence of disturbances.

## Slide 11
Simulation Results: Disturbed Case
The controller effectively rejects sensor noise without compromising tracking performance.

## Slide 12
Simulation Results: Robustness Analysis
The NMPC controller demonstrates accurate trajectory tracking and robustness against various perturbations.
8 cm
Default Case
9 cm
Disturbed Case
8 cm
Noisy Case
Force profiles adapt to compensate external disturbances and remain stable under noise.
Torques are modulated to ensure attitude stability, with noise introducing noticeable fluctuations.

## Slide 13
Simulation Results: Robustness analysis
The NMPC controller demonstrates accurate trajectory tracking and robustness against various perturbations.
Default Case
Disturbed Case
Noisy Case

## Slide 14
Conclusions & Future Developments
The NMPC controller effectively minimizes errors and rejects disturbances, demonstrating strong prediction capabilities.
Optimal State Observers
Integrate Kalman filters to reduce steady-state errors.
Adaptive Elements
Improve performance in complex environments.
Obstacle Avoidance
Implement advanced collision prevention.
Battery Handler
Develop for real hardware implementation.

## Slide 15
Thank you for your attention!